Technical Information sheet

RTI Installation Notes

   Installation Notes
- At the main enclosure terminate the Cat 5 cable using an RJ45 plug (according to the 586B convention) and patch into the appropriate socket in the patch panel
- All ports are labeled on the diagram in the main enclosure

At the sensor end the cable is terminated on a punch down connection (according to the 586B convention).

Technical Notes

The RTI is a resistive temperature sensor interface designed to give a 0-5V signal over the input range -50 to 200°C.

On the WebBrick the RTI is connected to an analogue input.

  Installation Diagram

  Intelligent Building Automation

For Support contact:

01635 897 301

or email: info@webbricksystems.com