Technical Information sheet

Room Controller Installation Notes

   Installation Notes
- Two Cat 5 cables are used for the room controller unit
- At the zone hub or main enclosure terminate both of the Cat 5 cables using an RJ45 plug (according to the 586B convention) and patch into the appropriate port in the patch panel
- All ports are labeled on the diagram in the zone hub or main enclosure
- At the room controller terminate both of the Cat 5 cables using an RJ45 plug (according to the 586B convention) and patch into the port as follows:
    - Connect the Cat 5 'A' from the zone hub or main controller to 'A' on the room controller
    - Connect the Cat 5 'B' from the zone hub or main controller to 'B' on the room controller
  Note: The two Cat 5 cables are identified by A and B. Make sure that A is connected to A and B is connected to B from the zone hub or main enclosure to the room controller

Technical Notes

The room controller is powered on its own circuit and only control signals are provided from the zone hub or main enclosure.

  Installation Diagram

  Intelligent Building Automation

For Support contact:

01635 897 301

or email: info@webbricksystems.com