Technical Information sheet

Villavent HRV Unit Installation Notes

Intelligent Building Automation

For Support contact:

01635 897 301

or email: info@webbricksystems.com
  Installation Diagram

  Intelligent Building Automation

For Support contact:

01635 897 301

or email: info@webbricksystems.com

   Installation Notes
Two Cat 5 cables are allocated for control and monitoring of the Villavent HRV unit but only one is used at the moment
- At the main enclosure terminate one of the Cat 5 cables using an RJ45 plug (according to the 586B convention) and patch into the appropriate port in the patch panel
- All ports are labeled on the diagram in the main enclosure
- At the Villavent HRV unit the Cat 5 that was terminated in the main enclosure is terminated as follows:
  - all striped cores are connected to 'G'
  - the blue core is connected to channel 1
  - the green core is connected to channel 2
  - the orange core is connected to channel 3
  - the brown core can be connected to channel 4 or can be left unconnected
- The Outputs (Contacts) of the Villavent Driver need to be connected as follows to the control board of the Villavent unit:
  - Contact 1 to DI 1
  - Contact 2 to DI 2
  - Contact 3 to DI 3
  - C (Common) to Ground